## Slide 1: My lights don’t blink and flash, help!
Les Willis
WillisChristmasShow.com

## Slide 2: My background
Electrical Engineer - retired
Programmer
Many years experience with
    Computers
    Networking
    DIY

## Slide 3: My lighting background
GCLF
  Great Christmas Light Fight
2016 took the full plunge into smart RGB pixels
Always have had a static light display
2015 Season I did my first light animation to music (using dumb RGB and incandescent)

## Slide 4: I Heard the Bells on Christmas Day

## Slide 5: What makes up a light show?
Props
  RGB Pixels (low voltage DC)
  Incandescent (120 AC)
  DMX devices (moving heads, smoke machines)
Controllers
Computer

## Slide 6: Basic network setup
Cont 1
Cont 2
Cont 3
Computer
Router

## Slide 7: Controllers
LOR
Falcon
Pis/Hats
Beagles/Capes

## Slide 8: Basic network setup
Computer
Router
Controller

## Slide 9: Logical flow
Computer
Router
Sequence
Software
Controller
Lights

## Slide 10: Punch list (items to check)
Double check your controller/prop connection
“Ping” your controller/verify network connection
Utilize test features in your controller
Confirm/set controller settings (port, interface, channel/universe
Verify the above settings in your sequence software (controller type, IP address, universes)
Utilize the test features in your sequence software
Start sequencing!

## Slide 11: 1. Check prop connections
Wrong
Pinched insulation
Wrong
Loose wire
Right!
Newer Pixels don’t use
CLK connection

## Slide 12: Find controller IP address
Log into your router
Look on the controller if it will display this
Make sure IP address does not change!

## Slide 13: 2. Ping your controller
Use the Windows “Command Window” and “Ping” program

## Slide 14
3. Use test features in controller
4. Confirm settings (Universes and ports)

## Slide 15: Logical flow
Computer
Router
Sequence
Software

## Slide 16
5. Verify settings in your sequence program
6. Use your program’s test features

## Slide 17: Check list review
Double check your controller connection to your pixel string(s)
“Ping” your controller (verify network connection
Utilize test features in your controller
Confirm controller settings (port, interface, channel/universe
Verify the above settings in your sequence software (controller type, IP address, universes)
Utilize the test features in your sequence software
Start sequencing!

## Slide 18: Questions?